## Slide 1
Common data fields |  | These data fields are present for every asset type | 
Variable name | Label | Description | Data type
FEATURE_ID | Feature ID | Unique ID for asset | Character
SVDATE | Survey Date | Date asset was surveyed | Date
BOROUGH | Borough | London Borough in which asset is located | Character
LATITUDE | Latitude | Geographical reference of asset | Geometry coordinates
LONGITUDE | Longitude | Geographical reference of asset | Geometry coordinates
PHOTO1_URL | Photo1 URL | URL for asset photo 1 | Character
PHOTO2_URL | Photo2 URL | URL for asset photo 2 | Character
geometry | Geometry | A spatial tibble of simplefeatures | sfc_MULTILINESTRING
Latitude and longitude converted to simple features geometry

## Slide 2
Advanced Stop Lines |  | Advance stop lines (ASL) are located at traffic signals to provide an area for cyclists to wait for the traffic signals to change ahead of the general traffic. The ASL reservoir is the area between the solid stop line, level with the signals, and the ASL for general traffic. The reservoir may have a coloured surface and have a cycle symbol in the centre. | 
Variable name | Label | Description | Data type
ASL_FDR | Feeder Lane | True = Feeder lane present False = No feeder lane present (may be gate) | Character
ASL_FDRLFT | Feeder Lane on Left | True = Feeder lane is aligned left next to kerb False = Feeder lane is not aligned left next to kerb | Character
ASL_FDCENT | Feeder Lane in Centre | True = Feeder lane is in the centre of the Advanced Stop Line False = Feeder lane is not in the centre of the Advanced Stop Line | Character
ASL_FDRIGH | Feeder Lane on Right | True = Feeder lane is aligned to far side of lane False = Feeder lane is not aligned to far side of lane | Character
ASL_SHARED | Shared Nearside Lane | True = Shared nearside lane False = Not a shared nearside lane | Character
ASL_COLOUR | Colour | Colour of advanced stop line - Limited to only the following entries: None, Green, Red, Blue, Buff/Yellow, Other | Character

## Slide 3
Crossings |  | Crossings intended to be used by cyclists. Crossings may be located at road junctions or in the middle of road links between junctions. This feature may include pedestrian-only crossings but only where they provide a link intended for cyclists to use between signed cycle routes (e.g. shared footways on both sides of the road or crossings over multi-lane, major or busy roads). | 
Variable name | Label | Description | Data type
CRS_SIGNAL | Signal-Controlled Crossing | True = Controlled False = Uncontrolled (e.g. zebra) | Character
CRS_SEGREG | Segregated cycles and Pedestrians | True = Cyclists segregated False = Shared with other users (e.g. pedestrians or horses) | Character
CRS_CYGAP | Cycle Gap | True = Crossing includes gap in island or kerb allowing cyclists only (NOT a refuge) False = Crossing does not include gap in island or kerb | Character
CRS_PEDEST | Pedestrian-Only Crossing | True = Cyclists must dismount to use False = Not a pedestrian-only crossing | Character
CRS_LEVEL | Level Crossing | True = Crossing or rail/tram tracks on cycle lane/track False = Not a level crossing | Character

## Slide 4
Cycle Lanes/Tracks |  | Formally designated road space for cyclists, usually identified with a combination of signs and line markings, and very often marked with the cycle symbol. Cycle lanes are parts of the road marked for use by cyclists. A bus lane that cyclists may use is regarded as a type of cycle lane. Cycle tracks are always off-carriageway, either next to it (associated with the footway) or completely away from the highway (e.g. canal towpaths, routes through parks). The ways that they are signed are more variable than cycle lanes | 
Variable name | Label | Description | Data type
CLT_CARR | On-Carriageway or Off-Carriageway | True = On-carriageway False = Off-carriageway | Character
CLT_SEGREG | Segregated Lane/Track | True = Fully segregated lane (i.e. On carriageway) / track (i.e. Off carriageway) False = Not fully segregated | Character
CLT_STEPP | Stepped Lane/Track | True = Stepped lane/track False = Not a stepped lane/track | Character
CLT_PARSEG | Partially Segregated Lane/Track | True = Partially or light segregated lane/track False = Not a partially or light segregated lane/track | Character
CLT_SHARED | Shared Lane or Footway | True = Shared lane (eg bus lane) False = Shared footway or track | Character
CLT_MANDAT | Mandatory Cycle Lane | True = Mandatory lane False = Not a mandatory lane | Character
CLT_ADVIS | Advisory Cycle Lane | True = Advisory lane False = Not an advisory lane | Character
CLT_PRIORI | Cycle Lane/Track Priority | True = Cycles have priority, other traffic has to give way False = Cycles do not have priority | Character
CLT_CONTRA | Contraflow Lane/Track | True = Contraflow lane/track (NOT if bi-directional) False = With flow | Character
CLT_BIDIRE | Bi-directional | True = Two way flow on lane/track/path False = Single direction lane/track/path | Character
CLT_CBYPAS | Cycle Bypass | True = Bypass allowing turn without stopping at traffic signals False = Not a cycle bypass | Character
CLT_BBYPAS | Continuous Cycle Facilities at Bus Stop | True = Cycle track carries on through the bus stop area False = Not a continuous cycle facility | Character
CLT_PARKR | Park Route | True = Road/lane/track through park False = Not a park route | Character
CLT_WATERR | Waterside Route | True = Route beside river, canal or other watercourse False = Not a waterside route | Character
CLT_PTIME | Part-time (if true) or Full-time (if false) | True = Part-time False = Full-time | Character
CLT_ACCESS | Access Times | Times route is accessible (either exact times or description) | Character
CLT_COLOUR | Colour | Colour of lane/track - Limited to only the following entries: None, Green, Red, Blue, Buff/Yellow, Other | Character

## Slide 5
Restricted route |  | Short linking routes or links that form part of signed/otherwise designated cycle routes that cyclists may use if they dismount. | 
Variable name | Label | Description | Data type
RES_PEDEST | Pedestrian-Only Route | True = Pedestrian-only route linking cycle routes False = Not a pedestrian-only route | Character
RES_BRIDGE | Pedestrian Bridge | True = Route includes a pedestrian bridge False = Route does not include a pedestrian bridge | Character
RES_TUNNEL | Pedestrian Tunnel | True = Route includes a pedestrian tunnel/subway False = Route does not include a pedestrian tunnel/subway | Character
RES_STEPS | Steps | True = Route includes steps to/from a particular cycle route which form part of a linear link route False = No steps | Character
RES_LIFT | Lift | True = Route includes lift to/from a particular cycle route which forms part of a linear link route False = No lift | Character

## Slide 6
Cycle Parking |  | Cycle parking assets such as cycle stands or racks to which cycles can be locked. In some locations cycle parking consists of lockers or a secure compound. | 
Variable name | Label | Description | Data type
PRK_CARR | Carriageway | True = On carriageway False = Off carriageway | Character
PRK_COVER | Covered | True = Covered or sheltered (including partial shelter) False = No cover | Character
PRK_SECURE | Secure | True = Locked compound with shared or combination lock provided by operator False = Not a locked compound | Character
PRK_LOCKER | Locker | True = Locker using own or integral lock False = No locker present | Character
PRK_SHEFF | Sheffield Stand | True = Sheffield stand (including TfL type) or variant False = Not a sheffield stand | Character
PRK_MSTAND | "M" stand | True = "M" stand (variety of stand that resembles a letter M) False = Not an "M" stand | Character
PRK_PSTAND | "P" stand | True = P, flag or pennant stand (variety of stand that resembles a letter P) False = Not a "P" stand | Character
PRK_HOOP | Cyclehoop | True = Cyclehoop False = Not a cyclehoop | Character
PRK_POST | Post | True = Post False = Not a post | Character
PRK_BUTERF | Butterfly | True = Butterfly/wheelbender False = Not a butterfly/wheelbender | Character
PRK_WHEEL | Wheel Rack | True = Wheel rack or slot False = Not a wheel rack or slot | Character
PRK_HANGAR | Bike Hangar | True = Bike hangar False = Not a bike hangar | Character
PRK_TIER | Two Tier | True = Multi tiered cycle parking False = Not a multi tiered cycle parking | Character
PRK_OTHER | Other | True = Other or unknown type of cycle parking False = Not an unknown type of cycle parking | Character
PRK_PROVIS | Provision | Number of stands or discrete units | Character
PRK_CPT | Capacity | Number of bikes that can be parked without difficulty | Character

## Slide 7
Restricted point |  | Restricting elements such as steps or lifts. | 
Variable name | Label | Description | Data type
RST_STEPS | Steps | True = This feature is only relevant where steps link routes where cycling is permitted. False = No steps | 
RST_LIFT | Lift | True = This feature is only relevant where a lift links routes where cycling is permitted. False = No lift | 

## Slide 8
Signage |  | Signs and markings that provide information to cyclists about where they are going, where they can/cannot cycle and what space has been designated for their specific use, adding to the sense of safety and accessibility. Only those signs relevant to cycling are included. | 
Variable name | Label | Description | Data type
SS_ROAD | Road Marking or Sign Face | True = Road marking or symbol False = Sign face | Character
SS_PATCH | Coloured Patch on Surface | True = Marking/symbol on coloured background patch False = No colour | Character
SS_COLOUR | Colour of Patch | Colour of road marking patch | Character
SS_FACING | Facing Off-side | True = Facing oncoming traffic but on off-side (i.e. right) False = Not facing oncoming traffic | Character
SS_NOCYC | No Cycling | True = Sign prohibiting cycling (No Cycling) False = Sign not prohibiting cycling | Character
SS_NOVEH | No Vehicles | True = No vehicles except pedal cycles pushed False = Sign not prohibiting vehicles | Character
SS_CIRC | Circular Sign or Rectangular Sign | True = Circular False = Rectangular | Character
SS_EXEMPT | Exemption | True = Exemption text present (i.e. "Except cycles") False = No exemption text | Character
SS_NOLEFT | No Left Turn Exception | True = Banned left turn with exception False = No banned left turn | Character
SS_NORIGH | No Right Turn Exception | True = Banned right turn with exception False = No banned right turn | Character
SS_LEFT | Compulsory Turn Left Exception | True = All traffic must turn left with exception False = No compulsary left turn | Character
SS_RIGHT | Compulsory Turn Right exception | True = All traffic must turn right with exception False = No compulsary right turn | Character
SS_NOEXCE | No Straight Ahead Exception | True = Banned straight ahead movement with exception False = Straight ahead movement not banned | Character
SS_DISMOU | Cyclists Dismount | True = Cyclist dismount sign False = Not a dismount sign | Character
SS_END | End of Route | True = End of route sign False = Not an end of route sign | Character
SS_CYCSMB | Cycle Symbol | True = Cycle symbol or marker False = Cycle symbol or market not present | Character
SS_PEDSMB | Pedestrian Symbol | True = Pedestrian symbol False = Pedestrian symbol not present | Character
 |  |  | Character
SS_BUSSMB | Bus Symbol | True = Bus symbol False = Bus symbol not present | Character
SS_SMB | Other Vehicle Symbol | True = Taxi/Motorcycle/Horse symbol False = Taxi/Motorcycle/Horse symbol not present | Character
SS_LNSIGN | Delineating Line on Sign | True = Delineating line False = Delineating sign not present | Character
SS_ARROW | Direction Arrow | True = Contraflow or one-way False = Not contraflow or one-way | Character
SS_NRCOL | Number in a Box | True = Yes a number in a box is present False = Number is box isn't present | Character
SS_NCN | National Cycle Network | True = National Cycle Network sign, symbol or sticker False = Not a National Cycle Network sign, symbol or sticker | Character
SS_LCN | London Cycle Network | True = London Cycle Network sign or symbol False = Not a London Cycle Network sign or symbol | Character
SS_SUPERH | Cycle Superhighway | True = Cycle Superhighway sign, symbol or marker (NOT totem) False = Not a Cycle Superhighway sign, symbol or marker | Character
SS_QUIETW | Quietway | True = Quietway sign or symbol False = Not a Quietway sign or symbol | Character
SS_GREENW | Greenway | True = Greenway sign, symbol or marker False = Not a Greenway sign, symbol or marker | Character
SS_ROUTEN | Route Number | Number of route | Character
SS_DESTN | Destination | True = Direction sign False = Advisory sign | Character
SS_ACCESS | Access Times | Times route is accessible (either exact times or description) | Character
SS_NAME | TSRGD Sign Number | Sign number, e.g. 956.1, 953.1A, | Character

## Slide 9
Signal |  | Traffic signals where there are specific benefits for cyclists. These include signals that have been designed or reprogrammed so that the phasing gives advantage to cyclists and improves their safety moving through the junction. | 
Variable name | Label | Description | Data type
SIG_HEAD | Cycle Signal Head | True = Cycle symbol on signal (as a light/set of lights with symbols) False = No cycle symbol on signal | Character
SIG_SEPARA | Separate Stage for Cyclists | True = Separate stage for cyclists False = No separate stage for cyclists | Character
SIG_EARLY | Early Release | True = Early release for cyclists False = No early release for cyclists | Character
SIG_TWOSTG | Two Stage Turn | True = Two stage right turn (where signed) False = No two stage right turn (where signed) | Character
SIG_GATE | Cycle/Bus Gate | True = Cycle/bus gate allowing cycles to get ahead of traffic False = Not a cycle/bus gate | Character

## Slide 10
Traffic calming |  | Traffic calming measures are intended to reduce the speed of motor vehicles. They generally comprise of vertical and/or horizontal deflections. Traffic calming assets were recorded for on-carriageway features only. For example, speed humps on fully segregated cycle lanes would not be captured. | 
Variable name | Label | Description | Data type
TRF_RAISED | Raised Table | True = Raised table at junction False = Not a raised table | Character
TRF_ENTRY | Side Road Entry Treatment | True = Side road entry treatment (raised in some way including continuous footway) False = Not a side road entry treatment | Character
TRF_CUSHI | Speed Cushions | True = Speed cushions in line across road False = Not a speed cushions in line across road | Character
TRF_HUMP | Speed Hump | True = Speed hump False = Not a speed hump | Character
TRF_SINUSO | Sinusoidal | True = Hump or cushion is sinusoidal False = Not a sinusiodal hump or cushion | Character
TRF_BARIER | Barrier | True = Barrier that cyclists can pass False = No barrier | Character
TRF_NAROW | Carriageway Narrowing | True = Chicane, narrowing, build-out or other horizontal deflection to traffic flow False = No carriageway narrowing | Character
TRF_CALM | Other | True = Other traffic calming measure False = No an 'other' type of traffic calming | Character